Logistical Header	Source Card Type	[Data Frame 1]	[Data Frame 2]	[Data …]	[Data Frame n]

0	4 8 16 24 32 n
Logistical Header:
Logistical Request	→	(0x0) Used to poll Followers for information.
Logistical Response	→	(0x1) Responds to Logistical Request. Followed by yes/no data	frame.
Error	→	(0x2) Used to report an error.
Data	→	(0x3) Used to send non-logistical data.

Acknowledgement	(0x4) Sent to follower devices to say message was received
Boot	(0x5) When booting up sends information to slave
Interrupt	(0x6) Allows for slaves to interrupt connection
Command Request	(0x7) request to send a command to Follower device
        Command Response	(0x8) Responds to receive message of command (acknowledges before performing the command

Logistical Request Format
0b0000	Source Card Type

0 4 8
This is sent to a slave to ask if there is any message for the master to read from it. The slave will always respond with a logistical response. If the Logistical Request times out, it will be viewed as an error. In such a timeout case, the slave may be assumed non-responsive or not installed into the motherboard and may be taken out of the communication update loop.

Logistical Response Format
0b0001	Source Card Type	(0b0 / 0b1) , Buffer Size

0 4 8 9 16
This is sent back to the master in response to a Logistical Request. It contains only the Logistical Header and one 8-bit data frame. The first bit in the data frame answers a yes or no to the question. 0 indicates that there is data to read from the slave, while a 1 indicates that there is not. The remaining 7 bits in this data frame denote the amount of sequential bits of data to be read. Since I2C reads 8-bit data frames, rather than direct bits, it is suggested that any data is built in 8 bit blocks, though extra bits can simply be ignored.

Error

0b0010	Source Card Type	Error Type

0	4	8	16
The Error Header is used to report an error to the master. Error Type is an 8-bit data frame that denotes the error code. These error codes will be card specific, so they can only be defined as part of the card design. Since there are 16 reportable card types and one 8-bit data frame for the error code, it’s suggested that error codes are defined by card type as denoted below, though this isn’t required.

Card Type	Error Code Range	Card Type	Error Code Range
0	0-4095	8	32768-36863
1	4096-8191	9	36864-40959
2	8192-12287	A	40960-45055
3	12288-16383	B	45056-49151
4	16384-20479	C	49152-53247
5	20480-24575	D	53248-57343
6	24576-28671	E	57344-61439
7	28672-32767	F	61440-65535

Data
4-wire AC (Card Type 0x2)
Input
0b0011	4 wire AC (card)	Specific Card Data ---- >

0	4	8	48

4 - Wire AC (Card Data)
Channel number	On/Off	Voltage flag	Range	32-bit Resistance data
0b000	0b0	0b0	0b000	0b0000 0000 0000 0000…. 0000
0b001
0b010
0b011

8	11	12	13	16	48

Channel number:
4 channels each on will contain a setting for whether the channel will be on or off and what the range that channel will be.

On/Off:

1 value for on
0 Value for off

Voltage flag:

Using the extra byte from the range to be a voltage flag. When 1 it means the number is returning a voltage when low it is returning a resistance value

Range:
Range

0	4

Represent the possible range of resistance that can be used by the 4 wire ac. This uses only three bits originally it was 4 with a buffer zero value but the extra zero bit is now going to be used a Boolean to represent if the data being received is a voltage or a resistance.

Flag	000	10K Ω
	001	100KΩ
	010	1MΩ
	011	10MΩ

0	1	4

16 bit Resistance Data
If we are using decimal numbers in returning back resistance values then the

*Changed to 32 bits precision of byte data*

This is intended to be a scientific notation of data
8 bits to represent the whole number with 24 bits of decimal point precision using mantissa binary numbers
Some bits will be reserved to represent as an exponential value.
Currently we can used the last 8 bits of the 24 decimal point precision as exponential (max value of 255) or signed bit ( 127 to -128)

Higher resistance is needed for when it gets below 1 K due to self heating
Difference modes when different resistors are attached to the 4 wire ac card

The card will have to convert the voltage or resistance into scientific notation. The scientific notation of the conversion will be displayed onto the GUI.

4 Channels
Measuring 4 temperatures (change in resistance) uses 16 bits of double precision
Returns a resistance that ranges from ~100ohm to 100Kohm

Error:
Time out
Could not detect master – time out
Could not understand master request
Value in sent to device does not make sense

Boot
0b0100	Source card

0	4	8
The initial message the master sends out for slaves to respond to. The slaves are to respond with their typical logistical response with what card they are but they will have no data attached to them, so they will send all zeros. On this initial boot the Master will wait for a response from each possible card and then add each card to the round Robin while loop if the corresponding source card responds within a certain time limit. There is a possible of 10 max cards so the increment of the source card number will max at 10 (Actually at 0b0111)

Interrupt

0b0101	Source Card Type	Interrupt data

0	4	8	16
Triggers an interrupt to happen to allow the card to break the master out of the Round Robin. It has the interrupt trigger and what source card and telling the master what it wants to do. The master will handle the Interrupt before going back to what it was doing. Once the interrupt is finished the master will continue its while loop rounds of all the cards registered as slaves, checking for information.

Command Request
0b0111	Source card type	Command type list

This will be used by the Leader device to send to Follower to have them perform a command
Possible commands to be used (functions vary from card to card):
Shutdown
Change settings
Temp
Voltage or resistance data
Resistance range

Command Response
0b1000	Source card type	Data?

0	4	8
An acknowledgement that the card has received the command.
(card will acknowledge After doing command)
Not sure if a data portion is going to be needed could be used as something similar to logistical requestion to write if the card has any new data to report after the command has been executed. (NOTE: if data portion is not needed then the acknowledgement can be send before performing the command. This data can also instead be sent as either a regular round robin or a interrupt instead)