## Slide 1
H.aHKBox Chassis
&
Hardware Interface Communications
Adam Stammer
Under the Direction of Dr. Carl Ferkinhoff

## Slide 2
Design Steps
Define the Problem
Research
List Requirements
Brainstorm Solutions
Choose Solution
Develop Solution
Prototype
Test and Redesign
Communicate Results

## Slide 3: Radioastronomy

## Slide 4
What is ZEUS2?
Designed by Dr. Carl Ferkinhoff (~2009)
Radio Telescope
  Submillimeter grating spectrometer
  Observer emission lines in all submillimeter bands accessible from the ground
Notes: 4

## Slide 5
What’s the Problem?
Rather Old
No Longer Supported by Manufacturer
Superfluous
Clunky
Occasionally Malfunctioned

## Slide 6
The Project
Abstract Goals
To design and build an open source, modular Eurocard system to be used as astronomical control/housekeeping equipment
To replace existing ZEUS2 housekeeping equipment with a cheaper, simpler, more robust system
Design Steps
Design Prototyping Daughtercard (P-Card)
Design Eurocard Backplane to connect and control modular cards
Choose Power Supplies
Choose Chassis
Manufacture
Program Embedded Controllers
Notes: 6

## Slide 7
Whiteboarding of the H.aHK Box

## Slide 8
Draft model of H.aHK Box
Blue = touch screen
Black = power supply
Grey = cooling fan
Green = circuit boards (big is the bus, and slam are the cards)

## Slide 9
Device | Processor | RAM/ Storage | Other | Software | Ref.
Raspberry Pi 3 $39.95 | 64-bit 1.2 GHz ARM | 1 GB/ 32GB | 40GPIO, SPI, I2C, HDMI, 4 - USB, Ethernet, Serial | Debian Linux | [5]
Teensy 3.2 $19.80 | 72 MHz ARM Cortex-M4 | 64KB/ 256 KB | 34 GPIO, 21 ADC (13-Bit), Serial (3), SPI, I2C (2), | Arduino IDE | [6]
Similar cases and cards as the H.aHK Box as found commercially.

## Slide 10
Prototyping Card (P-Card)
Sketch
Male Socket, Female Socket, Breadboard, High Power Banana Jacks, Double Length For Easy Access

## Slide 11
Sockets
60 Pins @ 2 Amps and 4 High Current Pins @ 20 Amps

## Slide 12
Socket Pinout
2 HP IO, 9 4pin IO Channels, 2 I2C Channels, 1 SPI Channel, Low Power Input, High Power Input, Ground

## Slide 13
Prototyping Card (P-Card)
Male Socket, Female Socket, Breadboard, High Power Banana Jacks, Double Length For Easy Access

## Slide 14
Prototyping Card (P-Card)
Male Socket, Female Socket, Breadboard, High Power Banana Jacks, Double Length For Easy Access

## Slide 15
Backplane
Simplified
Schematic
Sketch
Sockets, Power, SPI, HP Signal I/O, 9 4-pin signal I/Os per card, Arduino Controller (with I2C), On board Temperature Sensors, 7-segment digit display, 5Volt and 20Volt Power, Raspberry Pi (with I2C), Interrupts from Arduino and Pi

## Slide 16
Backplane
Schematic
Sockets, Power, SPI, HP Signal I/O, 9 4-pin signal I/Os per card, Arduino Controller (with I2C), On board Temperature Sensors, 7-segment digit display, 5Volt and 20Volt Power, Raspberry Pi (with I2C), Interrupts from Arduino and Pi

## Slide 17
Backplane
Schematic
Closeup
Sockets, Power, SPI, HP Signal I/O, 9 4-pin signal I/Os per card, Arduino Controller (with I2C), On board Temperature Sensors, 7-segment digit display, 5Volt and 20Volt Power, Raspberry Pi (with I2C), Interrupts from Arduino and Pi
A
C
B

## Slide 18
Chassis Render
Front

## Slide 19
Chassis Render
Back

## Slide 20
Card Render

## Slide 21
Microcontrollers
What is a Microcontroller?
Dedicated Single-Task Computers
Small
Low Power
Low Cost
Dedicated Input
Example Uses
Smart Devices
Motor Controller
Thermostat
Remote Control

## Slide 22
Next Steps
Finish Technical Guide
Summary of Completed Work
Guide Future Designers and End Users
Finish Backplane PCB Layout
Manufacture
Program Controllers
Capacity Tests
Design/Build Cards

## Slide 23
Microcontrollers
Communication Example
-200°C
Cooler Controller
Temperature Sensor
Arduino
Raspberry Pi
Touchscreen
ZEUS2

## Slide 24
Embedded Systems Communication
Protocols
Purpose
To communicate data between separate pieces of hardware
Components
Data
Timer
Power
Interface
Wire
Circuit Board
Wireless
Active/Passive
Inter/Intra
Shared/Dedicated Bus

## Slide 25
Core Considerations
Inter vs. Intra System Communication
Inter – Communication between two separate systems
e.g. Computer to Arduino or Cell Phone
Intra – Communication between two dependent systems
usually on the same circuit board
e.g. Temperature Sensors to CPU on PC Motherboard
Shared vs. Dedicated Bus
Shared – Multiple Devices on the same BUS allows for fewer wires but adds complexity (What happens when two devices talk at the same time?)
Dedicated – Each devices gets it’s own BUS/Data Line
Active vs. Passive
Passive – Common Data Bus written to and read from as necessary (Like holding up a sign)
Active – Always listening on Data Bus for ‘sent’ message (Like Verbal Speech)

## Slide 26
Universal Asynchronous Receive/Transmit
Turn Parallel Data into Successive Data
Advantages
Asynchronous – no clock
Only Uses Two Wires
  Transmit (TX)
  Receive (RX)
Parity Bit for Error Checking
Disadvantages
One to One Communication
baud Rates must be very similar
  Common speed bottleneck
Examples
Predecessor to USB (Mouse and Keyboard)
Arduino Serial Output
Network Equipment
UART

## Slide 27
Serial Peripheral Interface
Fast Communication Between One and Many
  Designed for computer peripherals
Advantages
Continues (not packet based)
Simple Addressing of Slaves
Very Fast Communication
Separate Send/Receive Lines
One to Many Communication
Disadvantages
4 Wires Required
  Clock Signal
  Slave Select Even When Unnecessary
No Integrity or Message Received Checks
Only allows for One Master
Examples
SD Card Readers
Wireless Modules
RFID Readers
SPI

## Slide 28
Inter-Integrated Chip
Any Grouping Design But Intended For Many Sensors on the Same Circuit Board
Advantages
Only 2 Wires Regardless of How Many Slaves/Masters
Many to Many Possible
Acknowledgements ensure success
Very Common Protocol
Disadvantages
Not Very Fast
Small Frame Size
  High Overhead
Examples
OLED Displays
Temperature Sensors
Accelerometer/Gyroscope
I2C, I²C

## Slide 29
https://www.circuitbasics.com/
https://www.arduino.cc/
https://www.raspberrypi.org/
https://sites.google.com/site/carlferkinhoff/welcome-1 (thanks Carl)
http://hosting.astro.cornell.edu/~spifiweb/zeus2/index.html
Sources