## Slide 1
H.aHKBox Chassis
&
Hardware Interface Communications
Adam Stammer
Under the Direction of Dr. Carl Ferkinhoff

## Slide 2
Motivations
Obsolete Internal Chips
Multiplexer Readout Rate Limit
Dependent On PC

## Slide 3
Goals
Abstract Goals
Open Source
Modular-Card System
Cheap
Versatile
Design Steps
Prototyping Daughtercard (P-Card)
Backplane
ZEUS2 Daughtercards
Chassis and Accompanying Components
Communication Programming

## Slide 4
Draft Model
Blue = touch screen
Black = power supply
Grey = cooling fan
Green = circuit boards (big is the bus, and slam are the cards)

## Slide 5
Device | Processor | RAM/ Storage | Other | Software | Ref.
Raspberry Pi 3 $39.95 | 64-bit 1.2 GHz ARM | 1 GB/ 32GB | 40GPIO, SPI, I2C, HDMI, 4 - USB, Ethernet, Serial | Debian Linux | [5]
Teensy 3.2 $19.80 | 72 MHz ARM Cortex-M4 | 64KB/ 256 KB | 34 GPIO, 21 ADC (13-Bit), Serial (3), SPI, I2C (2), | Arduino IDE | [6]
Similar cases and cards as the H.aHK Box as found commercially.

## Slide 6
Sockets
60 Pins @ 2 Amps and 4 High Current Pins @ 20 Amps

## Slide 7
Prototyping Card (P-Card)
Sketch
Male Socket, Female Socket, Breadboard, High Power Banana Jacks, Double Length For Easy Access

## Slide 8
Male Socket, Female Socket, Breadboard, High Power Banana Jacks, Double Length For Easy Access
Prototyping Card (P-Card)
Sketch

## Slide 9
Ground Jumpers
High Power Input
IO Channel
High Power Output
Low Power Jumpers
Sockets
Space For
Solderless Breadboard(s)
P-Card PCB

## Slide 10
Backplane
Simplified
Schematic
Sketch
Sockets, Power, SPI, HP Signal I/O, 9 4-pin signal I/Os per card, Arduino Controller (with I2C), On board Temperature Sensors, 7-segment digit display, 5Volt and 20Volt Power, Raspberry Pi (with I2C), Interrupts from Arduino and Pi

## Slide 11
Backplane
Schematic
Sockets, Power, SPI, HP Signal I/O, 9 4-pin signal I/Os per card, Arduino Controller (with I2C), On board Temperature Sensors, 7-segment digit display, 5Volt and 20Volt Power, Raspberry Pi (with I2C), Interrupts from Arduino and Pi

## Slide 12
Microcontrollers
Communication Example
-200°C
Cooler Controller
Temperature Sensor
Arduino
Raspberry Pi
Touchscreen
ZEUS2

## Slide 13
Next Steps
Finish Technical Guide
Summary of Completed Work
Guide Future Designers and End Users
Finish Backplane PCB Layout
Manufacture
Program Controllers
Capacity Tests
Design/Build Cards

## Slide 14
https://www.circuitbasics.com/
https://www.arduino.cc/
https://www.raspberrypi.org/
https://sites.google.com/site/carlferkinhoff/welcome-1 (thanks Carl)
http://hosting.astro.cornell.edu/~spifiweb/zeus2/index.html
Sources