Logistical Header	Source Card Type	[Data Frame 1]	[Data Frame 2]	[Data …]	[Data Frame n]

0	4 8 16 24 32 n
Logistical Header:
Logistical Request	→	(0x0) Used to poll slaves for information.
Logistical Response	→	(0x1) Responds to Logistical Request. Followed by yes/no data	frame.
Error	→	(0x2) Used to report an error.
Data	→	(0x3) Used to send non-logistical data.

Logistical Request Format
0b0000	Source Card Type

0 4 8
This is sent to a slave to ask if there is any message for the master to read from it. The slave will always respond with a logistical response. If the Logistical Request times out, it will be viewed as an error. In such a timeout case, the slave may be assumed non-responsive or not installed into the motherboard and may be taken out of the communication update loop.

Logistical Response Format
0b0001	Source Card Type	(0b0 / 0b1) , Buffer Size

0 4 8 16
This is sent back to the master in response to a Logistical Request. It contains only the Logistical Header and one 8-bit data frame. The first bit in the data frame answers a yes or no to the question. 0 indicates that there is data to read from the slave, while a 1 indicates that there is not. The remaining 7 bits in this data frame denote the amount of sequential bits of data to be read. Since I2C reads 8-bit data frames, rather than direct bits, it is suggested that any data is built in 8 bit blocks, though extra bits can simply be ignored.

Error

0b0010	Source Card Type	Error Type

0	4	8	16
The Error Header is used to report an error to the master. Error Type is an 8-bit data frame that denotes the error code. These error codes will be card specific, so they can only be defined as part of the card design. Since there are 16 reportable card types and one 8-bit data frame for the error code, it’s suggested that error codes are defined by card type as denoted below, though this isn’t required.

Card Type	Error Code Range	Card Type	Error Code Range
0	0-4095	8	32768-36863
1	4096-8191	9	36864-40959
2	8192-12287	A	40960-45055
3	12288-16383	B	45056-49151
4	16384-20479	C	49152-53247
5	20480-24575	D	53248-57343
6	24576-28671	E	57344-61439
7	28672-32767	F	61440-65535

Data
4-wire AC (Card Type 0x2)
Input